Test Protocol – Field Testing

Engines/Trucks

The engines selected will be separated into two categories; i.e., a Control Group and a Candidate Group.  The Control Group will use untreated diesel fuel throughout the scope of the project.  The Candidate Group will receive Viscon-treated fuel.

A minimum of 10-15 engines for the Control Group and 10-15 engines for the Candidate Group will be selected.  The preference is 15 (or more, if obtainable) engines for the Candidate Group.  Testing with fewer engines will not provide statistically valid test data.  If some of the engines have mechanical problems or respond marginally, the test results may be deemed unsuccessful.

Baseline-1; establishes a reference/starting point, for the untreated Control and Candidate groups

Duration: 50 hours or 1 month

- Capture operational hours/mileage and fuel added to the tank for EACH fueling – For Heavy Equipment, record idling time.

- Compute total fuel used by hour/mile for each engine.

- Maintain a running/cumulative fuel used average by engine for each fueling (to identify +/- trends).

- Record averages grouped by Control v. Candidate groups.

- At completion of the baseline, compute a ratio (factor/difference) between the Control and Candidate groups.

Viscon Treatment; captures data for the treated Candidate Group and untreated Control Group

Duration: 150 hours or 3 months

- Capture operational hours/mileage and fuel added (and the amount of Viscon added for the Candidate engines) to the tank for EACH fueling – For Heavy Equipment, record idling time.

- Compute total fuel used by hour/mile for each engine.

- Maintain a running/cumulative fuel usage average by engine for each fueling starting at the Viscon Treatment point (to identify +/- trends).

- Maintain a percent change from Baseline for each engine and each fueling (Control & Candidate).

- Maintain a running/cumulative percent change from Baseline for each engine (Control & Candidate) as they relate to their Baseline data; i.e., determine the change from Baseline for each engine.  Changes from Baseline, especially for the Control group may indicate changes in operations, weather, etc.  The resulting change/ratio may be applied to the Candidate engine results as an adjustment factor.

- Record averages grouped by Control v. Candidate groups.

Baseline-2 (Optional); provides data relative to returning to baseline/residual effects after treatment has been completed

Duration: 50 hours or 1 month

- Capture operational hours/mileage and fuel added to the tank for EACH fueling

- Record data for individual engines and averages grouped by Control v. Candidate groups.

- Compute total fuel used by hour/mile for each engine.

- Maintain a running/cumulative fuel used average by engine for each fueling (to identify +/- trends).

- At completion of the baseline, compute a ratio (difference) between the Control group during Treatment and the Control group during Baseline-2.

Attachments:

Fuel Consumption Log Sheet (for data capturing)

Sample Spreadsheet (for computations and reporting)

| Fuel Consumption Log Sheet | Page:______ |
| --- | --- |
| Business Name: . | Viscon California |
| Contact Info.: | Viscon Rep: _____________ |
| Phone #: | Phone: _____________ |

| Engine |
| --- |
| Engine ID |  | Make |  | Model |  |
| Year |  | HP |  | Hrs/Gal/Ltr |  |

| Date Fueled | Hrs/Odom Reading | Amount of Fuel Added | Amount of Viscon Added | Oper. Maintenance Records / Notes / Initl’s Heavy Equip.- Record Idling Time |
| --- | --- | --- | --- | --- |

#### 1 Ounce of Viscon to 20 Gallons of Fuel

#### -- For “manually” introducing Viscon into the fuel, Pre-Mix for optimal results --

Pre-Mix Viscon:  Example - Measure amount of Viscon required – add Viscon to 2/3 – 3/4 gallons of fuel in a one-gallon container – shake moderately for 2-3 minutes – add solution to fuel tank.

##### Add Viscon to fuel tank level BEFORE fueling

Fueling after adding Viscon to the tank will better incorporate Viscon via “Splash-Blending.”

The splashing effect of the fueling facilitates the Viscon/fuel blending.

Record a minimum of 20 data points/fueling each for Baseline & Treatment.

Engine ID# 										  Engine Make													Model 										Year 									Horsepower

BASELINE-1

--Running Average--

Net										Fuel/									 @ Baseline Start

Hrs 					Hours 		Fuel 				Hour/													Percent

Date						Odom			Odom		Added			Gal														Change

mm/dd/yy		99999				99999			9999.9			99.99														99.99%

mm/dd/yy		99999				99999			9999.9			99.99														99.99%

mm/dd/yy		99999				99999			9999.9			99.99														99.99%

Totals			      							99999			9999.9			99.99

TREATMENT

--Running Average--			--Running Average--

Net										Fuel/										@ Treatment Start				  From Baseline

Hrs 					Hours 		Fuel 				Hour			Amt of										Percent							Percent

Date						Odom			Odom		Added			Gal				Viscon			Fuel					Change							Change

mm/dd/yy		99999				99999			9999.9			99.99				99.9			Start “Running Averages” After 3-4 Fill-Ups

mm/dd/yy		99999				99999			9999.9			99.99				99.9

mm/dd/yy		99999				99999			9999.9			99.99				99.9				99.9						99.9%									99.9%

Treatment Totals				  99999			9999.9			99.99

Baseline Totals					  99999			9999.9			99.99

% Change																						99.9%

Baseline (Control v. Candidate) Factor				 9.9%

% Change																						99.9%

Treatment (Control v. Control) Factor				 9.99

% Change																						99.9%

BASELINE-2

--Running Average--			--Running Average--		--Running Average--

Net										Fuel/										@ Baseline-2 Start				 From Baseline-1				 From Treatment

Hrs 				Hours 		Fuel 				Hour			Amt of										Percent							Percent										Percent

Date						Odom			Odom		Added			Gal				Viscon			Fuel					Change							Change										Change

mm/dd/yy		99999				99999			9999.9			99.99				99.9				99.9						99.9%									99.9%												99.9%

mm/dd/yy		99999				99999			9999.9			99.99				99.9				99.9						99.9%									99.9%												99.9%

mm/dd/yy		99999				99999			9999.9			99.99				99.9				99.9						99.9%									99.9%												99.9%

Baseline Totals						99999			9999.9			99.99